"Thank you for your interest in Monroe products.  I've been able to dig up some old information and from that, match you a shock. The shock that I found matches physically and dimensionally, it is part number 66120. This shock is a cab shock for a heavy-duty truck. The 66120 extends at 8.50" and compresses at 6.50", the outer dirt shield diameter is 2.02" and reserve tube diameter 1.75". The dampening ability of the shock is also the same.  The only difference I encountered was in the mounting eyes. The original had 5/8" ID bushings and the 66120 has 12mm ID bushings. You will have to press out the bushings from the 66120 and replace them with bushing number 45540 (this can be special-ordered through your local NAPA Auto Parts store)."